SUBMERSIBLE PRESSURE TRANSDUCER:

The submersible transducer shall be a two wire device operating on 10-30VDC supply with a 4-20mA level signal.  The transducer shall have a temperature range of -10 to 70 degrees C or 14 - 158 degrees F and have an inaccuracy of minimum plus or minus 0,1 % of total range. The transducer shall be cable suspended and not dependent upon position.  The probe housing shall have Ryton PPS (polyphenylene sulfide) plastic encapsulation, the vented cable be of polyurethane, the membrane protection holes of large size to prevent clogging and the diaphragm be of 99,9 % pure ceramic. The transducer shall be a Flygt LTU 801.