SUBMERSIBLE PRESSURE TRANSDUCER:

The submersible transducer shall be a two wire device operating on 6-27VDC supply with a 4-20mA level signal or ModBus and with auto-zero function.  The transducer shall have a temperature range of -20 to 80 degrees C or -4 - 176 degrees F and have an inaccuracy of minimum plus or minus 0,35 % of total range. The transducer shall be cable suspended and not dependent upon position.  The membrane protection holes shall be of large size to prevent clogging and the diaphragm protected by a cover. The transducer shall be a Flygt LTU 403.